Business Rule Engine
Detailed Listing of Actions

Overview
This document contains a detailed listing of the available actions for the Business Rule Engine „Jare“. It lists the available data types, their combinations and possible optional or required parameters.
Actions are defined on the rulegroup level. When a rulegroup fails or passes then none, one or multiple actions can be executed. Actions are executed in the sequence that they have been defined. It is also possible to define actions that are execute when the rulegroup passes and actions when the rulegroup fails at the same time.
A condition must be specified when to execute the action – when the rulegroup fails or passes. Additionally a field - and it's type - must be specified that will be updated by the action.
Sometimes an action will require additional values to be passed to it. This can either be the value of another field or a defined fixed value.
The values selected in the action from “Field to retrieve data”, “Parameter 1”, “Parameter 2” and “Parameter 3” are passed to the action in this sequence. The “Field to retrieve data” is optional and indicates from which other field a value should be retrieved. It can be specified but must not be.
If for example the action requires two values (arguments) then either “Field to retrieve data” and “Parameter 1” have to be specified or alternatively “Parameter 1” and “Parameter 2” (and “Field to retrieve data” is left blank). Then in turn the “Field to update” will be updated with the resulting value.

Prerequisites
The default date format used is: yyyy-MM-dd. If not otherwise specified for String to Date conversions, it is assumed that the value is provided in this format. Date formats need to be according to the Java SimpleDateFormat Class format definitions.
All data types listed here are Java related data types.

Add Leading Spaces
Purpose:	Add leading spaces to a value until a given length of the value is reached
Java Class:	StringAction
Interface Name:	add leading spaces

Applicable to:
Value 1	Value 2
String	Integer
Note:
Optional Value(s)	Explanation

Add Leading Zeros
Purpose:	Add leading zeros to a value until a given length of the value is reached
Java Class:	StringAction
Interface Name:	add leading zeros

Applicable to:
Value 1	Value 2
String	Integer
Note:
Optional Value(s)	Explanation

Append Value
Purpose:	Append a given value to the end of another value
Java Class:	StringAction
Interface Name:	append

Applicable to:
Value 1	Value 2
String	String
Note:
Optional Value(s)	Explanation
Value 3: String	Separator to be used between the values

Prepend Value
Purpose:	Prepend a given value to the start of another value
Java Class:	StringAction
Interface Name:	prepend

Applicable to:
Value 1	Value 2
String	String
Note:
Optional Value(s)	Explanation
Value 3: String	Separator to be used between the values

Trim Value
Purpose:	Remove all leading and trailing space characters from a String
Java Class:	StringAction
Interface Name:	trim

Applicable to:
Value 1	Value 2
String
Note:
Optional Value(s)	Explanation

Concat Values
Purpose:	Concatenate two values
Java Class:	StringAction
Interface Name:	append value

Applicable to:
Value 1	Value 2
String	Double
String	Float
String	Long
String	Integer
String	String
Note:
Optional Value(s)	Explanation
Value 3: String	Separator to be used between the value

Lowercase Value
Purpose:	Change a value to it's lowercase representation
Java Class:	StringAction
Interface Name:	lowercase

Applicable to:
Value 1	Value 2
String
Note:
Optional Value(s)	Explanation

Uppercase Value
Purpose:	Change a value to it's uppercase representation
Java Class:	StringAction
Interface Name:	uppercase

Applicable to:
Value 1	Value 2
String
Note:
Optional Value(s)	Explanation

Replace Value
Purpose:	Replace a given value – or part of it - with another value
Java Class:	StringAction
Interface Name:	replace

Applicable to:
Value 1	Value 2
String	String
Note: Value 2 has to contain a regular expression. All found occurrences of the regular expression will be replaced with value 3.
Required Value(s)	Explanation
Value 3: String	the replacement for the original value or parts of it

Set Value (String)
Purpose:	Sets a given value of a string
Java Class:	StringAction
Interface Name:	set value (string)

Applicable to:
Value 1	Value 2
String
Note:
Optional Value(s)	Explanation

Set Value (Date)
Purpose:	Sets a given value of a date
Java Class:	DateAction
Interface Name:	set value (date)

Applicable to:
Value 1	Value 2
String
Note:
Optional Value(s)	Explanation

Set Value (Number)
Purpose:	Sets a given value of a number
Java Class:	MathAction
Interface Name:	absolute

Applicable to:
Value 1	Value 2
Double
Float
Long
Integer
Boolean
Note:
Optional Value(s)	Explanation

Substring Value
Purpose:	Sets the value to a given substring
Java Class:	StringAction
Interface Name:	set value (String)

Applicable to:
Value 1	Value 2
String	Integer
Note: Value 2 defines from which position of the value the substring will start
Optional Value(s)	Explanation
Value 3: Integer	Defines at which position the substring will end

Set Todays Date
Purpose:	Set the value to the current date
Java Class:	DateAction
Interface Name:

Applicable to:
Value 1	Value 2
String
Note: Value 1 contains the date format to use
Optional Value(s)	Explanation
Value 2: Integer	Define an offset of days – positive or negative – that will be added to the current date

Absolute Value
Purpose:	Calculates the absolute value of a given value
Java Class:	MathAction
Interface Name:	absolute

Applicable to:
Value 1	Value 2
Double
Float
Long
Integer
Note:
Optional Value(s)	Explanation

Acosinus Value
Purpose:	Calculates the acosinus of a given value
Java Class:	MathAction
Interface Name:	acosinus

Applicable to:
Value 1	Value 2
Double
Note:
Optional Value(s)	Explanation

Cosinus Value
Purpose:	Calculates the cosinus of a given value
Java Class:	MathAction
Interface Name:	cosinus

Applicable to:
Value 1	Value 2
Double
Note:
Optional Value(s)	Explanation

Cosinush Value
Purpose:	Calculates the cosinush of a given value
Java Class:	MathAction
Interface Name:	cosinush

Applicable to:
Value 1	Value 2
Double
Note:
Optional Value(s)	Explanation

Asinus Value
Purpose:	Calculates the asinus of a given value
Java Class:	MathAction
Interface Name:	asinus

Applicable to:
Value 1	Value 2
Double
Note:
Optional Value(s)	Explanation

Sinus Value
Purpose:	Calculates the sinus of a given value
Java Class:	MathAction
Interface Name:	sinus

Applicable to:
Value 1	Value 2
Double
Note:
Optional Value(s)	Explanation

Sinush Value
Purpose:	Calculates the sinush of a given value
Java Class:	MathAction
Interface Name:	sinush

Applicable to:
Value 1	Value 2
Double
Note:
Optional Value(s)	Explanation

Atangens Value
Purpose:	Calculates the atangens of a given value
Java Class:	MathAction
Interface Name:	atangens

Applicable to:
Value 1	Value 2
Double
Note:
Optional Value(s)	Explanation

Tangens Value
Purpose:	Calculates the tangens of a given value
Java Class:	MathAction
Interface Name:	tangens

Applicable to:
Value 1	Value 2
Double
Note:
Optional Value(s)	Explanation

Tangensh Value
Purpose:	Calculates the tangensh of a given value
Java Class:	MathAction
Interface Name:	tangensh

Applicable to:
Value 1	Value 2
Double
Note:
Optional Value(s)	Explanation

Square Root Value
Purpose:	Calculates the square root of a given value
Java Class:	MathAction
Interface Name:	square root

Applicable to:
Value 1	Value 2
Double
Note:
Optional Value(s)	Explanation

Square Value
Purpose:	Calculates the square of a given value
Java Class:	MathAction
Interface Name:	square

Applicable to:
Value 1	Value 2
Double
Float
Long
Integer
Note:
Optional Value(s)	Explanation

Add Values
Purpose:	Calculates the sum of two values
Java Class:	MathAction
Interface Name:	sum

Applicable to:
Value 1	Value 2
Double	Double
Float	Float
Integer	Integer
Integer	Long
Long	Integer
Long	Long
Note:
Optional Value(s)	Explanation

Subtract Values
Purpose:	Subtracts two values
Java Class:	MathAction
Interface Name:	subtract

Applicable to:
Value 1	Value 2
Double	Double
Float	Float
Integer	Integer
Integer	Long
Long	Integer
Long	Long
Note:
Optional Value(s)	Explanation

Devide Values
Purpose:	Calculates the devision of two values
Java Class:	MathAction
Interface Name:	devide

Applicable to:
Value 1	Value 2
BigDecimal	BigDecimal
Double	Double
Double	Integer
Float	Float
Integer	Integer
Integer	Long
Long	Integer
Long	Double
Long	Long
Note:
Optional Value(s)	Explanation

Multiply Values
Purpose:	Multiplies two values
Java Class:	MathAction
Interface Name:	multiply

Applicable to:
Value 1	Value 2
Double	Double
Double	Integer
Float	Float
Integer	Integer
Integer	Long
Long	Double
Long	Integer
Long	Long
Note:
Optional Value(s)	Explanation

Round Value
Purpose:	Rounds a given value
Java Class:	MathAction
Interface Name:	round

Applicable to:
Value 1	Value 2
Double
Float
Note:
Optional Value(s)	Explanation